## Slide 1: A Framework For Integrating Pedestrians into Travel Demand Models
Kelly J. Clifton
Civil Engineering Department Seminar
Monash University
July 14, 2017

## Slide 2: Portland, Oregon, USA
City
25th largest in US
Population ~ 640k
Area ~ 376 km2
Density ~ 1,689/km2
Region
Population~ 2.4 M
Urban Growth Boundary
Only elected regional government in US

## Slide 3: Portland, Oregon

## Slide 4: Transportation @ PSU
8 transport faculty in Civil Engineering & Urban Studies & Planning
Transportation Research & Education Center (TREC) administers:
  The National Institute for Transportation & Communities, one of 5 centers funded by U.S. Department of Transportation. Focus on improving mobility of people and goods to build strong communities.
  The Initiative for Bicycle and Pedestrian Innovation, which shares active transportation insight with professionals and educators.
  TREC hosts weekly transportation seminars and offers live and archived streaming: http://trec.pdx.edu/professional-development

## Slide 5: My Research Group
Travel behavior & built environment
  Residential Location
  Active travel
  Planning applications & modelling tools
  Behavioral theory
  Smart cities applications
  Equity
  Assessing transport impacts of new development
  Data collection methods
http://kellyjclifton.com

## Slide 6: Outline
A Framework For Integrating Pedestrians into Travel Demand Models
Policy & planning context
MoPeD – Model of Pedestrian Demand
Opportunities & challenges
  Behavioral research
  Data & models
Future directions

## Slide 7: Policy & planning Context

## Slide 8: Why model pedestrians?
Pedestrian investments
Mode shifts
Greenhouse gas emissions
Health & safety
Transit access/egress
New research opportunities

## Slide 9: State of the Practice
1. Generation
2. Distribution
3. Mode choice
4. Assignment
Trip-based model sequence
How do travel models estimate walking?
Source: Singleton, P. A., & Clifton, K. J. (2013). Pedestrians in regional travel demand forecasting models: State-of-the-practice.
Among 48 large MPOs in US:
  38% did not estimate walking
  33% estimated non-motorized (walking + bicycling) travel
  29% estimated walking
Lacking pedestrian built environment measures & small spatial units

## Slide 10: Incorporating pedestrians
Ready
Challenging
Most Challenging
Adapted from: Wegener and Fürst, 1999

## Slide 11: Incorporating pedestrians
Ready
Adapted from: Wegener and Fürst, 1999

## Slide 12: Model of Pedestrian Demand Moped

## Slide 13: Project overview
12 years of research/development in modeling pedestrian demand
Recent research projects funded by NITC and Portland Metro
  Improve representation of pedestrians in current 4-step method
  Develop stand alone tool
  Transferability & forecasting of built environment measures

## Slide 14: New MoPeD method
TAZ = transportation analysis zone
PAZ = pedestrian analysis zone
Trip Generation (PAZ)
Trip Distribution or Destination Choice (TAZ)
Mode Choice (TAZ)
Trip Assignment
Pedestrian Trips
Walk Mode Split (PAZ)
Destination Choice (PAZ)
I
III
All Trips
Pedestrian Trips
Vehicular Trips

## Slide 15: Contributions
Nests within current structure but can be used alone
Pedestrian scale analysis (PAZs)
Pedestrian-relevant variables (PIE)
One of the first studies to examine pedestrian destination choice in demand modeling framework
Highlights policy relevant
variables: distance, size,
pedestrian supports &
barriers

## Slide 16: Pedestrian analysis zones
264 feet = 80 m ≈ 1 minute walk
Metro: ~2,000 TAZs  ~1.5 million PAZs
TAZs
PAZs
Home-based work trip productions

## Slide 17: Pedestrian environment
Pedestrian Index of the Environment (PIE)
20–100 score = calibrated ∑(6 dimensions)
ULI = Urban Living Infrastructure: pedestrian-friendly shopping and service destinations used in daily life.
People & job density
Transit access
Block size
Sidewalk extent
Comfortable facilities
Urban living infrastructure

## Slide 19: Trip Generation
TAZ = transportation analysis zone
PAZ = pedestrian analysis zone
Trip Generation (PAZ)
Trip Distribution or Destination Choice (TAZ)
Mode Choice (TAZ)
Trip Assignment
Pedestrian Trips
Walk Mode Split (PAZ)
Destination Choice (PAZ)
I
III
All Trips
Pedestrian Trips
Vehicular Trips

## Slide 20: Trip Generation
Metro currently has 8 trip production models applied to ~2,000 TAZs:
  HBW – Home-based work;
  HBshop – Home-based shopping;
  HBrec – Home-based recreation;
  HBoth – Home-based other (excludes school and college);
  NHBW – Non-home-based work;
  NHBNW – Non-home-based non-work;
  HBcoll – Home-based college; and
  HBsch – Home-based school.
After testing for scalability, we applied the same models to our pedestrian scale ~1.5M PAZs

## Slide 22: Walk mode split
TAZ = transportation analysis zone
PAZ = pedestrian analysis zone
Trip Generation (PAZ)
Trip Distribution or Destination Choice (TAZ)
Mode Choice (TAZ)
Trip Assignment
Pedestrian Trips
Walk Mode Split (PAZ)
Destination Choice (PAZ)
I
III
All Trips
Pedestrian Trips
Vehicular Trips

## Slide 23: Walk mode split
Prob(walk) = f(traveler characteristics, PIE)
Data: 2011 OHAS, Production trip ends,
            90% sample
Method: binary logit model
Spatial unit: pedestrian analysis zone (PAZ)
Walk Mode Split (PAZ)
Pedestrian Trips
Vehicular Trips
II

## Slide 24
Walk mode split models
II
Traveler characteristics: Household size, income, age, # of workers, # children, # vehicles
Built environment: PIE

## Slide 25: Walk model application

## Slide 26: Destination choice
TAZ = transportation analysis zone
PAZ = pedestrian analysis zone
Trip Generation (PAZ)
Trip Distribution or Destination Choice (TAZ)
Mode Choice (TAZ)
Trip Assignment
Pedestrian Trips
Walk Mode Split (PAZ)
Destination Choice (PAZ)
I
III
All Trips
Pedestrian Trips
Vehicular Trips

## Slide 27: Destination choice

## Slide 28: Destination choice
Pedestrian Trips
Destination Choice (PAZ)
Prob(dest.) = function of…
  network distance
  size / # of destinations
  pedestrian environment
  traveler characteristics
Data: 2011 OHAS
Method: multinomial logit model
Spatial unit: super-pedestrian analysis zone
Six trip types: home-based: non-home-based:
work (HBW) work (NHBW)
shopping (HBS) non-work (NHBNW)
recreation (HBR)
other (HBO)
III

## Slide 29: Destination Choice

## Slide 30: Destination Choice
Model Validation – Avg. Distance Walked

## Slide 31: Opportunities & challenges Behavioral research/data/methods
Adapted from: Wegener and Fürst, 1999

## Slide 32: Behavioral research
Decision sequencing:
  activity, mode, destination;
  mode, destination, activity;
  destination, activity, mode
Destination choice considerations
  choice set generation
Willingness to walk
Path/route choice considerations

## Slide 33: Behavioral Research
Built environment
  Thresholds & nonlinearities
  Mixing
  Scale
Lifestyle questions:
  Vehicle ownership & residential location
  Attitudes, motivations & values
Positive Utility of Travel
  What aspects?
  Diminishing returns?
Mode feedbacks to trip generation

## Slide 34: Spatial/Temporal Scale
Depends on output needed for policy/research
Capture variations in the pedestrian built & natural environment
Spatial accuracy
Theory/Behavior

## Slide 35: Walking Behavior
Passive data sources
  Trip-level information
  Multi-day
  Multi-modal
  Destinations
  Routes & speeds
But also need…
  Motivations & considerations
  Barriers
  Trips not made

## Slide 36: Built environment
How & what to represent?
Indices, proxies
Forecasting
S.R. Gehrke, & K.J. Clifton. (2016). Toward a spatial-temporal measure of land-use mix. Journal of Transport and Land Use, 9(1):171–186
S.R. Gehrke, & K.J. Clifton. (2014). Operationalizing land use diversity at varying geographic scales and its connection to mode choice: Evidence from Portland, Oregon. Transportation Research Record: Journal of the Transportation Research Board 2453: 128-136.

## Slide 37: Networks
Network representation
How do we attribute networks?
Feedbacks of travel costs
Do we need to assign trips to a network?
Broach, J. P. (2016). Travel mode choice framework incorporating realistic bike and walk routes (Order No. 10061477). Available from Dissertations & Theses @ Portland State University; ProQuest Dissertations & Theses Global.

## Slide 38: Link to Health Outcomes
Health impact analysis
Total time spent walking + speeds
Physical activity budgets
Crash risk exposure
Pollutant exposure
Feedback into life expectancy
Woodcock J, Givoni M, Morgan AS. Health Impact Modelling of Active Travel Visions for England and Wales Using an Integrated Transport and Health Impact Modelling Tool (ITHIM). Barengo NC, ed. PLoS ONE. 2013;8(1):e51462

## Slide 39: Future directions
Pedestrian Environment
  Policy Sensitivity & Forecasting
Integration with ABM
Trip Generation
  Multinomial Logit model
Pedestrian mode choice
  Feedbacks to trip generation & destination choice
  Better representation of attributes of other modes
Destination Choice
  Explore non-linear effects & other interactions
Route choices or potential pathways
  Need fundamental research to improve understanding

## Slide 40: Future directions
Fellowship at Technical University of Munich
Collaborate with Dr. Rolf Moeckel
Incorporate pedestrians into regional integrated land use – transport model
Link to health assessment models
Recruiting funded PhD student (now!)

## Slide 41: Questions?
Kelly J. Clifton
kclifton@pdx.edu http://kellyjclifton.com
Project info & reports:
http://trec.pdx.edu/research/project/510
http://trec.pdx.edu/research/project/677
Singleton, P. A., Schneider, R. J., Muhs, C. D., & Clifton, K. J. (2014). “The Pedestrian Index of the Environment (PIE): Representing the Walking Environment in Planning Applications,” Proceedings of the 93rd Annual Meeting of the Transportation Research Board, 2014.
Clifton, K. J., Singleton, P. A., Muhs, C. D., & Schneider, R. J. 2016. “Representing pedestrian activity in travel demand models: Framework and applications”, Journal of Transport Geography, Vol. 52:111-122. http://dx.doi.org/10.1016/j.jtrangeo.2016.03.009.
Clifton, K. J., Singleton, P. A., Muhs, C. D., & Schneider, R. J. 2016. “Development of destination choice models for pedestrian travel”, Transportation Research Part A, 94: 255-265